IOM International Organization for Migration

OIM Organizaţia Internaţională pentru Migraţie

LIST OF REQUIREMENTS

VEHICLE SERVICING AND MAINTENANCE AND SUPPLY OF SPARE PARTS AND CONSUMABLES

FOR EUBAM “LAND ROVER” VEHICLES

GOAL

- Servicing and maintenance of the EUBAM “Land Rover Freelander 2” and “Land Rover Defender” vehicles pool in Moldova.

- Supply of genuine parts for servicing and maintenance works.

METHOD

- The Provider delivers vehicle servicing and maintenance services based on IOM/EUBAM claims.

- This type of services includes the planned regular maintenance, troubleshooting, replacement of parts/assemblies, as well as the general maintenance inspection in line with the manufacturer’s recommendations and any other necessary repair works according to the IOM/EUBAM claim.

- It is prohibited to conduct any repair works without a claim and the prior agreement with the IOM/EUBAM.

- The vehicle is delivered to the Provider’s workshop and taken back by the EUBAM drivers.

- Should there be faults in the vehicle that make it impossible to drive the vehicle to the workshop, the provider must deliver the vehicle to its workshop based on the IOM/EUBAM claim.

TERM OF AGREEMENT

IOM stipulates the conclusion of the Agreement with one provider of qualified vehicle maintenance and repair services with the tentative starting date of 1 July 2015 till 30 November 2015 with possibility of extension tentatively till 30 June 2016, provided EUBAM Mission mandate extended.

VOLUME OF PROVIDED SERVICES AND MAINTENANCE OF LAND ROVER FREELANDER 2/DEFENDER VEHICLES

Maintenance no.1

(conducted every 12,000 km of mileage)

| № | Work |
| --- | --- |
| 1 | Check tire pressure and tread depth (including the spare wheel) and alignment (if necessary). |
| 2 | Inspect the wear of brake pads, check if there is leakage in the calipers and check the disk condition. |
| 3 | Discharge the residues from the fuel filter. |
| 4 | Check the fluid level in the reservoirs of the brake system, hydraulic steering system, hydraulic clutch system and windshield washer and top-up if necessary. |
| 5 | Replace engine oil and filter. |
| 6 | Check the systems with IDS/SDD. |
| 7 | Reset the indicator informing about the maintenance interval. |
| 8 | Record the conducted maintenance. |

Maintenance no.2

# (conducted every 24,000 km of mileage)

| № | Work |
| --- | --- |
| 1 | Includes the works indicated in Maintenance no.1. |
| 2 | Check the condition and reliability of seats and safety belts. |
| 3 | Check the functionality of all lamps, sound signals and light indicators. |
| 4 | Check the functionality of front and rear wipers and washers and the condition of wiper brushes. |
| 5 | Check the functionality of parking brake. |
| 6 | Replace the pollen filter. |
| 7 | Replace fuel filter element. |
| 8 | Check and grease the hood latch. |
| 9 | Check the specific coolant density. |
| 10 | Replace the air cleaner element. |
| 11 | Check the condition of the driving belt of the auxiliary equipment. |
| 12 | Check the level /top-up battery electrolyte level. |
| 13 | Check the play of all silent blocks of the suspension. |
| 14 | Check the condition of all suspension covers and boots, driving shafts and steering. |
| 15 | Inspect the wear, leakage and corrosion of the brake servo amplifier hose, tube and muff of the brake and fuel systems, hydraulic steering system and clutch and garrots of the electric wiring. |
| 16 | Inspect fluid leakage. |
| 17 | Check the exhaust system for leakage, reliability of mountings and damages. |
| 18 | Check the mounting of tie rod ball joints and the condition of ball joints and protective boots. |

Other services

| № | Work |
| --- | --- |
| 1 | Inspect for corrosion / condition of the paint surface (every two years). |
| 2 | Replace the brake fluid (every 3 years). |
| 3 | Replace the coolant (every 10 years). |
| 4 | Replace the driving belt of the auxiliary equipment (every 120,000 km). |
| 5 | Replace the camshaft driving belt, belt tensioner and idle pulley (every 120,000 km). |
| 6 | Replace the oil in the manual gearbox (every 10 years). |
| 7 | Replace the oil in the transfer case (for Defender only) (every 10 years). |
| 8 | Replace the oil in the rear differential (every 10 years). |
| 9 | Replace the oil in the front differential (for Defender only) (every 10 years). |
| 10 | Replace the oil in the HALDEX system (for Freelander only) (every 10 years). |
| 11 | Replace all malleable hoses in the brake system (every 6 years). |

Services required for the following vehicles:

Type of vehicle				Quantity		Year of production

Land Rover Freelander 2	  	14			2008/2010

Land Rover Defender                                   1                                        2010

Based on the IOM/EUBAM claim, the provider must deliver the following additional services:

- Repair, painting or replacement of body parts;

- Repair or replacement of the vehicle interior equipment;

- Repair or replacement of parts and assemblies of the running gear, transmission and engine;

- Mounting/unmounting of communication equipment and other additional equipment (engine and interior heaters, hand luggage section grating, immobilizers, security system, etc.).

TERMS

- The claim for repair/maintenance must be filed with the provider at least 24 hours in advance.

- The planned maintenance, including maintenance no.1 and 2 must be conducted within one working day.

- All other services, repairs or maintenance works must be conducted in reasonable terms. If any delays are foreseen, the provider must inform the IOM/EUBAM.

- The term for supplying the parts based on the claim must not exceed:

a)  3 days – for the parts that are available at the storehouse;

b)  3 weeks – for the parts that are not available at the storehouse.

Minimum requirements:

Qualification of service provider:

Company profile: The offering party must make a short description of the company, including copies of company registration documents;

Detailed information on the work in this sphere: the offering party must submit a document that confirms at least 1 year of work experience in technical maintenance and repair of vehicles;

Amount of vehicles serviced in the previous year: at least 150;

Location: The offering party must have a workshop within the city of Chisinau, Moldova.

The provider must have the full set of equipment for diagnosing and repairing this type/model of vehicle.

Certificates:

The offering party must submit:

State registration certificate;

Copy of authorized or license in maintenance and repair services;

VAT payer’s certificate (if issued);

Duly accomplished vendor verification form;

Tax payer’s certificate;

Business reference:

The Provider must list analogical successful contracts and present the contacts of at least 2 corresponding reference entities;

The Seller must provide information on the personnel involved in the servicing/maintenance of this type/model of vehicles (are or not duly certified/trained).

Miscellaneous:

If the Provider is a Commercial Agent or Exclusive Distributor appointed by the vehicle manufacturer, the following certificates must be submitted:

- Powers from the manufacturer that give the company the right to act as a commercial agent.

- Certificate of the exclusive distributor in the country.

Quality control

- The Provider must have sufficient equipment and tools for servicing and maintenance that are adapted for the specific type/model of car.

- The Provider must have duly certified personnel to conduct servicing and maintenance works for the specific type/model of car.

- Only genuine parts must be used for servicing/maintenance. The parts must have standard warranty from the seller for 6 months or as indicated by the manufacturer (Land Rover).

- The warranty term from the service Provider for the conducted repair works must be at least 1 month.

Vehicle safety and security

- The Provider is liable for the vehicle safety and security, including the IOM equipment installed on the vehicle brought for servicing.

- The road tests must be carried out by the service Provider only in the presence of EUBAM drivers.

Documentation

- Any work conducted under the IOM/EUBAM claim must be indicated in the Deed on Performed Works that is presented immediately after the completion of work/maintenance and lists all the used parts plus the cost of works.

- The bill for servicing/maintenance must be submitted on a monthly basis and comprise the entire cost of works/services and parts provided to the IOM in the previous month.

- The cost of servicing/maintenance services and the cost of parts must be shown in separate lines of the account. The repair cost must include the cost of performed works based on the cost for one hour of work and the cost of parts.

IOM approves the bill for servicing/maintenance/transportation only if the works/maintenance were performed at a satisfactory level and in compliance with the manufacturer’s standards.

Organizational issues:

The offering party must present the name and contact details of the manager in charge for customer service or of another person in charge for the qualitative receipt and execution of IOM/EUBAM orders.

Assessment criteria and procedures:

The lowest cost among the bids that comply with technical requirements.

The costs will only be considered for the participants who comply with technical requirements (only the participants who comply with minimum technical requirements).

The agreement will be offered to the bidder who offers the lowest cost and has the necessary technical qualification and diligence.

Payment terms:

The payment for delivered services will be made through bank transfer on the bank account of the Agreement holder within 30 days from the day of service delivery and submission of the invoice for the delivered services.

In case if quotation submitted in US Dollars payments will be made in Moldovan Lei at the IOM Operational Rate of Exchange on the day of payment (link to the website with rates http://treasury.un.org/operationalrates/OperationalRates.aspx).

The price list must be presented in Moldovan Lei or US Dollars.

Please note that all prices must not include any taxes (VAT 0 rate), because the International Organization for Migration is exempt from taxes and duties as per Government Decision 246, dated 08.04.2010.

FORM FOR SUBMITTING SUPPLIER’S QUOTATION

(this form must be sent only with the official header / on the provider’s form)

We, the undersigned, hereby propose to deliver the goods/services listed below to you in compliance with the IOM technical characteristics and requirements set out in the Request for Proposals MD10-2015-019:

- The price list must comprise the detailed breakdown of costs for each item. The price list must be presented in Moldovan Lei or US Dollars.

- All the indicated prices/rates must not include taxes (VAT 0 rate), because the IOM is exempt from taxes and duties as per Government Decision 246, dated 08.04.2010.

- The format below must be used to devise the Price list. Please use only blank cells to input your information. The incorrectly filled in bids (in the table below) can be rejected.

Maintenance of Land Rover Freelander 2 vehicles

Type of services – Maintenance no.1

| No. | Work | Work length (min.) | Maximum cost of materials / parts | Maximum cost of works | Overall cost of works and materials / parts |
| --- | --- | --- | --- | --- | --- |
| 1 | Check tire pressure and tread depth (including the spare wheel) and alignment (if necessary). |  |  |  |  |
| 2 | Check the wear of brake pads, check if there is leakage in the calipers and check the disk condition. |  |  |  |  |
| 3 | Discharge the residues from the fuel filter. |  |  |  |  |
| 4 | Check the fluid level in the reservoirs of the brake system, hydraulic steering system, hydraulic clutch system and windshield washer and top-up if necessary. |  |  |  |  |
| 5 | Replace engine oil and filter. |  |  |  |  |
| 6 | Check the systems with IDS/SDD. |  |  |  |  |
| 7 | Reset the indicator informing about the maintenance interval. |  |  |  |  |
| 8 | Record the conducted maintenance. |  |  |  |  |
| Total for maintenance no.1 |  |

# Type of services – Maintenance no.2

| No. | Work | Work length (min.) | Maximum cost of materials / parts | Maximum cost of works | Overall cost of works and materials / parts |
| --- | --- | --- | --- | --- | --- |
| 1 | Includes the works indicated in Maintenance no.1. |  |  |  |  |
| 2 | Check the condition and reliability of seats and safety belts. |  |  |  |  |
| 3 | Check the functionality of all lamps, sound signals and light indicators. |  |  |  |  |
| 4 | Check the functionality of front and rear wipers and washers and the condition of wiper brushes. |  |  |  |  |
| 5 | Check the functionality of parking brake. |  |  |  |  |
| 6 | Replace the pollen filter. |  |  |  |  |
| 7 | Replace fuel filter element. |  |  |  |  |
| 8 | Check and grease the hood latch. |  |  |  |  |
| 9 | Check the specific coolant density. |  |  |  |  |
| 10 | Replace the air cleaner element. |  |  |  |  |
| 11 | Check the condition of the driving belt of the auxiliary equipment. |  |  |  |  |
| 12 | Check the level /top-up battery electrolyte level. |  |  |  |  |
| 13 | Check the play of all silent blocks of the suspension. |  |  |  |  |
| 14 | Check the condition of all suspension covers and boots, driving shafts and steering. |  |  |  |  |
| 15 | Inspect the wear, leakage and corrosion of the brake servo amplifier hose, tube and muff of the brake and fuel systems, hydraulic steering system and clutch and garrots of the electric wiring. |  |  |  |  |
| 16 | Inspect fluid leakage. |  |  |  |  |
| 17 | Check the exhaust system for leakage, reliability of mountings and damages. |  |  |  |  |
| 18 | Check the mounting of tie rod ball joints and the condition of ball joints and protective boots. |  |  |  |  |
| Total for maintenance no.2 |  |

Other services

| No. | Work | Work length (min.) | Maximum cost of materials / parts | Maximum cost of works | Overall cost of works and materials / parts |
| --- | --- | --- | --- | --- | --- |
| 1 | Inspect for corrosion / condition of the paint surface (every two years). |  |  |  |  |
| 2 | Replace the brake fluid (every 3 years). |  |  |  |  |
| 3 | Replace the coolant (every 10 years). |  |  |  |  |
| 4 | Replace the driving belt of the auxiliary equipment (every 120,000 km). |  |  |  |  |
| 5 | Replace the camshaft driving belt, belt tensioner and idle pulley (every 120,000 km). |  |  |  |  |
| 6 | Replace the oil in the manual gearbox (every 10 years). |  |  |  |  |
| 7 | Replace the oil in the transfer case (every 10 years). |  |  |  |  |
| 8 | Replace the oil in the rear differential (every 10 years). |  |  |  |  |
| 9 | Replace the oil in the HALDEX system (every 10 years). |  |  |  |  |
| 10 | Replace all malleable hoses in the brake system (every 6 years). |  |  |  |  |
| Total |  |  |  |

AGGREGATE TABLE

| Maintenance no.1 | Maintenance no.2 | Other | A- Overall cost of maintenance no.1, no.2 and other services |
| --- | --- | --- | --- |
| Overall number of maintenances | Maximum cost per unit | Total | Overall number of maintenances | Maximum cost per unit | Total | Overall number of services | Maximum cost per unit | Total |  |
| 24 |  |  | 24 |  |  | 10 |  |  |  |

Maintenance of Land Rover Defender vehicles

Type of services – Maintenance no.1

| No. | Work | Work length (min.) | Maximum cost of materials / parts | Maximum cost of works | Overall cost of works and materials / parts |
| --- | --- | --- | --- | --- | --- |
| 1 | Check tire pressure and tread depth (including the spare wheel) and alignment (if necessary). |  |  |  |  |
| 2 | Check the wear of brake pads, check if there is leakage in the calipers and check the disk condition. |  |  |  |  |
| 3 | Discharge the residues from the fuel filter. |  |  |  |  |
| 4 | Check the fluid level in the reservoirs of the brake system, hydraulic steering system, hydraulic clutch system and windshield washer and top-up if necessary. |  |  |  |  |
| 5 | Replace engine oil and filter. |  |  |  |  |
| 6 | Check the systems with IDS/SDD. |  |  |  |  |
| 7 | Record the conducted maintenance. |  |  |  |  |
| Total for maintenance no.1 |  |

# Type of services – Maintenance no.2

| No. | Work | Work length (min.) | Maximum cost of materials / parts | Maximum cost of works | Overall cost of works and materials / parts |
| --- | --- | --- | --- | --- | --- |
| 1 | Includes the works indicated in Maintenance no.1. |  |  |  |  |
| 2 | Check the condition and reliability of seats and safety belts. |  |  |  |  |
| 3 | Check the functionality of all lamps, sound signals and light indicators. |  |  |  |  |
| 4 | Check the functionality of front and rear wipers and washers and the condition of wiper brushes. |  |  |  |  |
| 5 | Check the functionality of parking brake. |  |  |  |  |
| 6 | Replace fuel filter element. |  |  |  |  |
| 7 | Check and grease the hood latch. |  |  |  |  |
| 8 | Check the specific coolant density. |  |  |  |  |
| 9 | Replace the air cleaner element. |  |  |  |  |
| 10 | Check the condition of the driving belt of the auxiliary equipment. |  |  |  |  |
| 11 | Check the level /top-up battery electrolyte level. |  |  |  |  |
| 12 | Check the play of all silent blocks of the suspension. |  |  |  |  |
| 13 | Check the condition of all suspension covers and boots, driving shafts and steering. |  |  |  |  |
| 14 | Inspect the wear, leakage and corrosion of the brake servo amplifier hose, tube and muff of the brake and fuel systems, hydraulic steering system and clutch and garrots of the electric wiring. |  |  |  |  |
| 15 | Inspect fluid leakage. |  |  |  |  |
| 16 | Check the exhaust system for leakage, reliability of mountings and damages. |  |  |  |  |
| Total for maintenance no.2 |  |

Other services

| No. | Work | Work length (min.) | Maximum cost of materials / parts | Maximum cost of works | Overall cost of works and materials / parts |
| --- | --- | --- | --- | --- | --- |
| 1 | Inspect for corrosion / condition of the paint surface (every two years). |  |  |  |  |
| 2 | Replace the brake fluid (every 3 years). |  |  |  |  |
| 3 | Replace the coolant (every 10 years). |  |  |  |  |
| 4 | Replace the driving belt of the auxiliary equipment (every 120,000 km). |  |  |  |  |
| 5 | Replace the camshaft driving belt, belt tensioner and idle pulley (every 120,000 km). |  |  |  |  |
| 6 | Replace the oil in the manual gearbox (every 10 years). |  |  |  |  |
| 7 | Replace the oil in the transfer case (every 10 years). |  |  |  |  |
| 8 | Replace the oil in the rear differential (every 10 years). |  |  |  |  |
| 9 | Replace the oil in the front differential (every 10 years). |  |  |  |  |
| 10 | Replace all malleable hoses in the brake system (every 6 years). |  |  |  |  |
| Total |  |  |  |

AGGREGATE TABLE

| Maintenance no.1 | Maintenance no.2 | Other | A- Overall cost of maintenance no.1, no.2 and other services |
| --- | --- | --- | --- |
| Overall number of maintenances | Maximum cost per unit | Total | Overall number of maintenances | Maximum cost per unit | Total | Overall number of services | Maximum cost per unit | Total |  |
| 2 |  |  | 2 |  |  | 1 |  |  |  |

Signature, stamp, date

# Footnotes

The official header/form must contain the contact information: addresses, electronic address, telephone and fax number for checking.